## Slide 1
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
CAD and Completed Assembly
I put in Mr. Alkins’ office waited to take photo tomorrow

## Slide 2
Date:11/17/25
Name: Jason Cao
Tool: 0.25x10Deg Taper
Stock: 5.5x 5.5 x0.75 Oak
Description: Mold Cavity
Part Reference: 26c016014A
MCS centered on top
Output from: Program Data Program Run: 09/18/2025 10:45:55 Linear Move Envelope: X: -2.425 2.455 Y: -2.442 2.455 Z: -0.390 0.500 Maximum Feedrate: 50.000 Maximum Spindle: 16000.000 Minimum Z at Rapid: -0.250
Jason Cao
Project 1 – Air Engine
Process Sheet for mold making
The design is made based on how to generate the largest inertia. Therefore, I left as much volume as I can. This design is also inspired from actual car wheels.

## Slide 3
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
CAD and Completed Assembly

## Slide 4
Jason Cao
Project 1 – Air Engine
Process Sheet for plasma cutting
The cut piece has rough edges on the top and bottom surface.
In order to fit the base with the backbone, I sanded the top surface making the edge is aligned with the smooth surface inside the edges.
Note: cut on Oct 30

## Slide 5
Date: 10/29/25
Name: Jason Cao
Description: Finish Flywheel
Stock: Cast Flywheel
Part Reference: 26c016022A
%
O0810 (PROGRAM)
( Date : Wed Oct 29 16:02:39 2025 )
( Programmer : 81969 )
( Part File Name: C:\Users\81969\OneDrive\Desktop\ME204\P1\cnc\26c016022A_setup_1.prt )
( Path Name : FACE_TURN )
(Tool Number: 2)
(Tool Name : CCGT431-HAL)
T0202
G97 S212 M3
G0 G54 X5.5 Z.25
Jason Cao
Project 1 – Air Engine
Process Sheet CNC Turining
The outside edge has an irregular indent. This is because when cast the flywheel with the mold, some places would cool faster causing the air bubble inside the mold. These air bubble would cause the incomplete formation which is the irregular indent.
Note: cut on Oct 30

## Slide 6
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
Process sheet CNC Milling
The CNC milling is very precise. I didn’t change any thing
after the process.
Note: cut on Oct 30

## Slide 7
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
Mechanism Simulation and Test
average pressure 3.32psi [1.60psi 5.24psi]
The differences in Cs is because of the drag force applied in simulation is not the real friction in the testing. The simulation only has drag force at the pin, but in the real testing, the friction also contains the hexagonal surface contacting with the backbone surface.
Cs difference with in 10%

## Slide 8
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
Composite Information
First, we put the 0 degree composite layer on the metal mold. Then, stack the 45 degree layer on the top of 0 degree. And put the -45 on the top of previous one. Finally, put another 0 degree layer on the top of -45 degree one. The directions would make the strength of the fiber layup higher because the 45 degrees can increase the resistance to shear forces and twisting forces. And the 0 degrees can carry the maximum tensile forces. By the superposition of the ply, it makes the strength of fiber layup higher.

## Slide 9
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
Drawing Package

## Slide 10
cylinder
fastener
backbone
Largest Hex size
Assy Tolerance Spring
bushing
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
Tolerance Stack Up
Min shoulder length
0.633 bmax+a+c
Note: Parts were modified for fit at assembly.
When I was assembling the rods to the crank, the rod was bended because the rod I used is slightly larger than the nominal size. I replaced the bended one to a new one and it works. Also, the dog doesn’t fit my flywheel, so I sanded the inner edges of the dog until they fit.
Min washer required
0.0083 bmax+a+c-fmin

## Slide 11
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
Moldability Checks
Radius added Edge Blend r = 0.02 in
Air Tap
Gate
Initial filling analysis shows no concerns

## Slide 12
Jason Cao
Nov 17, 2025
Project 1 – Air Engine
Assembly Sequence
Assembly Start
Completed Assembly