## Slide 1
Project 1, Team ALD (Lowe), Item 1
Body in Envelope Analysis Rendering
Curvature Analysis
Drafting Analysis

## Slide 2
Project 1, Team ALD (Lowe), Item 2
Date: 2/12/26
Name: Lowe
Tool: 1" Ball
Stock: 6.4" x 14.1" x 3"
Description: Mold for Body
Part Reference: 26c043357A
Feed Rate 50 ipm
Scallop Height 0.025"
MCS Center Bottom

## Slide 3
Project 1, Team ALD (Jason), Item 3
The test results mismatch the simulation results because the velocity in the wind tunnel is 50mph. What's more, the weight connected to the strain gage vibrated all the time causing a different result.

## Slide 4
Project 1, Team ALD (Lowe), Item 4
Solver type: Simcenter 3D Thermal/Flow
Analysis type: Flow
Solution type: Advanced Flow
Simulation File: Z:\205\P1\26c043370A_sim1.sim
Solution: Solution_1
Number of nodes in thermal model: 0
Number of elements in thermal model: 0
Number of nodes in flow model: 55281
Number of elements in flow model: 271149
Number of fluid nodes reused for surface coating: 5083
Number of elements created for surface coating: 9838
Solution Options
----------------
Steady-State Analysis
Solving Flow and Thermal
Ambient Temperature: 6.800E+01 F
Ambient Pressure: 1.470E+01 lbf/in^2
Gravitational Acceleration: 3.862E+02 in/s^2
Gravity Direction: X: 0.000E+00 Y: 0.000E+00 Z:-1.000E+00
Fluid buoyancy: Off
Flow solver type: Parallel
Parallel flow solver scheme: Fully Coupled Pressure-Velocity
Flow laminar/turbulent model: Spalart-Allmaras
Flow solver iteration limit: 1000
Flow converged when RMS residual less than: 2.000E-05
Flow solver physical time step: 5.000E-01 s
Flow solver heat imbalance: 2.000E-02
Advection Scheme Momentum: First Order
Advection Scheme Energy (if Solve_Energy): First Order
Advection Scheme Turbulence Model: First Order
Global Relaxation Factor: 7.500E-01
Mass Relaxation Factor: 7.500E-01
Fluids Relaxation Factor: 9.000E-01
Turbulence Relaxation Factor: 1.000E+00
Freeze flow field: Off
High Speed Flow: Off
Inlet 45mi/hr
Opening

## Slide 5
Project 1, Team ALD (Liao), Item 5
Team member scanning mold with FARO laser scanning tool
Geometry scanned in CAM2 software with deviation map
Colormap of geometry imported to NX, simplified
(Chordal Deviation 0.01”, Angle 0.5), compared to model

## Slide 6
Project 1, Team ALD (Jason Cao), Item 6
Solution: Nastran 101 Linear Static
Pressure load applied from Thermal Flow Analysis
Elements: CQUAD 4
Mesh size: 0.125''
Material: ABS (NX)
Thickness: 0.03''
Fixed constraint on the bottom edge
Structural response for 0.03'' ABS from CFD Loading
Transferred Pressure Load from CFD
Displacement filed due to pressure
The bottom is cut by 0.1 '' to make sure the geometry is clean

## Slide 7
Project 1, Team ALD (Liao), Item 7
Gravity Car – Initial Wheel Design
All Components PVC
Gravity Car – Improved Wheel Design
Improvement:
All Components PVC

## Slide 8
Project 1, Team ALD (Jason Cao), Item 8

## Slide 9
Project 1, Team ALD (Groeschel), Item 9
1. Original design of car shape.
2. Tool path for creation of mold.
3. Mold in wind tunnel.
4. Pressure plot in CFD simulation.
6. Pressure load and displacement of moldable body
7. Gravity car with improved wheel design.
The measured drag coefficient is ~94.3% different from the simulated drag coefficient. This may be caused by the difference in real shape to the ideal part that is simulated, the conditions of the wind tunnel not being equal to that of the simulation (i.e. the wind speed being different), or some mechanical error in the wind tunnel.
Error
5. Colormap of geometry of scanned mold.

## Slide 10
Project 1, Team ALD (Liao), Item 0
Tyler created the assembly and procured all the “bought” parts

## Slide 11
Project 1, Team ALD (Jason Cao), Item 0
26c016060A
#1 – Phone Holder
Part Info Version: 1.0 File Name: 26c016060A.prt Description: Phone Holder Version: 38 Last Save:02 Mar 26 14:38 Author:ccao10

## Slide 12
Project 1, Team ALD (Jason Cao), Item 0
26c016061A
#2 – Wheel
Part Info Version: 1.0 File Name: 26c016061A.prt Description: Wheel Version: 38 Last Save:02 Mar 26 15:59 Author:ccao10

## Slide 13
Project 1, Team ALD (Jason Cao), Item 0
26c016061A
#3 – Battery Chamber
Part Info Version: 1.0 File Name: 26c016062A.prt Description: Battery Chamber Version: 38 Last Save:02 Mar 26 16:15 Author:ccao10

## Slide 14
Project 1, Team ALD (Jason Cao), Item 0
26c016063A
#4 – Coupling
Part Info Version: 1.0 File Name: 26c016063A.prt Description: Coupling Version: 36 Last Save:02 Mar 26 16:15 Author:ccao10

## Slide 15
Project 1, Team ALD (Lowe), Item 0
26c043353A
#5 – Build Plate
Part Info Version: 1.0
File Name: 26c043353A.prt
Description: BUILD PLATE
Version: 39
Last Save:19 Feb 26 19:07
Author:clowe4

## Slide 16
26c029702B
#6 – Steering Pin
Part Info Version: 1.0
File Name: 26c029702B.prt
Description: STEERING PIN
Version: 41
Last Save:24 Feb 26 17:39
Author:hgroe
Project 1, Team ALD (Groeschel), Item 0

## Slide 17
26c029700B
#7 - Axel
Part Info Version: 1.0
File Name: 26c029700B.prt
Description: AXEL
Version: 40
Last Save:24 Feb 26 17:28
Author:hgroe
Project 1, Team ALD (Groeschel), Item 0

## Slide 18
26c029701B
#8 - Frame
Part Info Version: 1.0
File Name: 26c029701B.prt
Description: FRAME
Version: 43
Last Save:24 Feb 26 17:31
Author:hgroe
Project 1, Team ALD (Groeschel), Item 0

## Slide 19
26c043354A
#9 – Chassis Standoff
Part Info Version: 1.0
File Name: 26c043354A.prt Description: CHASSIS STANDOFF Version: 37
Last Save:19 Feb 26 19:20 Author:clowe4
Project 1, Team ALD (Lowe), Item 0

## Slide 20
26c029703A
#10 – Wheel Pin
Part Info Version: 1.0
File Name: 26c029703B.prt
Description: WHEEL PIN
Version: 42
Last Save:24 Feb 26 17:40
Author:hgroe
Project 1, Team ALD (Groeschel), Item 0